## Slide 1: Bluetooh Low Energy
2014.10.27, joey tseng

## Slide 2: Configurations between BT. versions
v4.0
BLE enabling
Dual Mode
Single Mode
Classic

## Slide 3: Limitations
Data throughput: 1 Mbps (Upper limitation)
Consecutive connection event interval : 7.5 ms ~ 4 S
Operation range: 30 meters, typical range is 2~5 meters.

## Slide 4: Network Topology
Brocaster
Observer
Observer
Send none connectable advertising packets
Scan none connectable advertising packets
VS
T1: Broadcasting & Observering
CENTRAL Device (Phone, Tablet)
PERIPHERAL Device
PERIPHERAL Device
Sends connectable advertising packets
1..n
1..n
1..n
1..n
T2: Connection
Scans connectable advertising packets
Device can be CETERAL or PERIPHERAL at the same time
Notes: None connectable means the form of connection is not 1 by 1
The differences between Protocols and profiles
Protocols
Building blocks used by all devices conformant to the Bluetooth specification, protocols
are the layers that implement the different packet formats, routing, multiplexing,
encoding, and decoding that allow data to be sent effectively between peers.
Profiles
“Vertical slices” of functionality covering either basic modes of operation required
by all devices (Generic Access Profile, Generic Attribute Profile) or specific use
cases (Proximity Profile, Glucose Profile), profiles essentially define how protocols
should be used to achieve a particular goal, whether generic or specific.

## Slide 5: Protocol Stack of BLE
APPLICATION
Link Layer
LE Phisical Layer
Generic Access Profile (GAP)
Generic Attribute Profile (GATT)
Security Manager Protocol (SMP)
Attribute Protocol (ATT)
Logical Link Control and Adaption Protocol (L2CAP)
Host Controller Interface (HCI)
HOST
Controller
Application
Notes: Link layer has:
Advertiser
A device sending advertising packets.
Scanner
A device scanning for advertising packets.
Master
A device that initiates a connection and manages it later.
Slave
A device that accepts a connection request and follows the master’s timing.

## Slide 6: Protocol Stack of BLE
APPLICATION
Link Layer
LE Phisical Layer
Generic Access Profile (GAP)
Generic Attribute Profile (GATT)
Security Manager Protocol (SMP)
Attribute Protocol (ATT)
Logical Link Control and Adaption Protocol (L2CAP)
Host Controller Interface (HCI)
APPLICATION
Link Layer
LE Phisical Layer
Generic Access Profile (GAP)
Generic Attribute Profile (GATT)
Security Manager Protocol (SMP)
Attribute Protocol (ATT)
Logical Link Control and Adaption Protocol (L2CAP)
Host Controller Interface (HCI)
Low level interaction
Actual data transfer procedures and formats

## Slide 7: GATT Internal
GATT
Profiles
Services
Characteristics
Descriptors

## Slide 8: GATT Internal - Sample
 |  |  | HANDLE | UUID | Permissions | Value
Service | Characteristics |  | 0x0021 | SERVICE | READ | HRS
 |  |  | 0x0024 | CHAR | READ | NOT¦0x0027¦HRM
 |  | Descriptors | 0x0027 | HRM | NONE | bpm
 | Characteristics |  | 0x0028 | CCCD | READ/WRITE | 0x0001
 |  |  | 0x002A | CHAR | READ | RD¦0x002C¦BSL
 |  |  | 0x002C | BSL | READ | finger